## Slide 1: FET Biasing

## Slide 2
MOSFETs
Be able to perform a dc analysis of JFET, MOSFET networks.
Become proficient in the use of load-line analysis to examine FET networks.
Develop confidence in the dc analysis of networks with both FETs and BJTs.
Understand how to use the Universal JFET Bias Curve to analyze the various FET configurations

## Slide 3
MOSFETs
For the field-effect transistor, the relationship between input and output quantities is nonlinear due to the squared term in Shockley’s equation.
A graphical approach may limit solutions to tenths-place accuracy, but it is a quicker method for most FET amplifiers
Since the graphical approach is in general the most popular, the analysis of this chapter will have graphical solutions rather than mathematical solutions.
The controlling variable for a BJT transistor is a current level, whereas for the FET a voltage is the controlling variable.

## Slide 4
FETs Biasing
The general relationships that can be applied to the dc analysis of all FET amplifiers are
For JFETs
For enhancement-type MOSFETs
It is particularly important to realize that all of the equations above are for the field effect transistor only !
They do not change with each network configuration so long as the device is in the active region.
The network simply defines the level of current and voltage associated with the operating point through its own set of equations.
In reality, the dc solution of BJT and FET networks is the solution of simultaneous equations established by the device and the network

## Slide 5
FIXED-BIAS CONFIGURATION
The simplest of biasing arrangements for the n -channel JFET
Referred to as the fixed-bias configuration, it is one of the few FET configurations that can be solved just as directly using either a mathematical or a graphical approach.

## Slide 6
FIXED-BIAS CONFIGURATION

## Slide 7
FIXED-BIAS CONFIGURATION
Applying Kirchhoff’s voltage law in the clockwise direction of the indicated loop
Since VGG is a fixed dc supply, the voltage VGS is fixed in magnitude, resulting in the designation “fixed-bias configuration.”

## Slide 8
FIXED-BIAS CONFIGURATION
The resulting level of drain current ID is now controlled by Shockley’s equation
Since VGS is a fixed quantity for this configuration, its magnitude and sign can simply be substituted into Shockley’s equation and the resulting level of ID calculated.
mathematical solution to a FET configuration
ID = ?

## Slide 9
FIXED-BIAS CONFIGURATION
The resulting level of drain current I D is now controlled by Shockley’s equation

## Slide 10
FIXED-BIAS CONFIGURATION
The dc levels of ID and VGS that will be measured by the meters of Fig. 7.5
Drain-to-source voltage of the output section
The fact that VD = VDS and VG = VGS is fairly obvious from the fact that VS = 0 V

## Slide 11
FIXED-BIAS CONFIGURATION
Determine the following for the network

## Slide 12
FIXED-BIAS CONFIGURATION
Determine the following for the network
How about Graphical Approach?

## Slide 13
FIXED-BIAS CONFIGURATION
Graphical Approach
The resulting Shockley curve and the vertical line at VGS = -2 V

## Slide 14
SELF-BIAS CONFIGURATION
The self-bias configuration eliminates the need for two dc supplies. The controlling gate to- source voltage is now determined by the voltage across a resistor RS introduced in the source leg of the configuration
JFET self-bias configuration.

## Slide 15
SELF-BIAS CONFIGURATION
JFET self-bias configuration.
IG = 0 A
The current through RS is the source current IS, but IS = ID and VRS = IDRS
Note in this case that VGS is a function of the output current ID and not fixed in magnitude as occurred for the fixed-bias configuration.
Shockley’s equation relates the input and output quantities of the device.
Both equations relate the same two variables, ID and VGS, permitting either a mathematical or a graphical solution.

## Slide 16
SELF-BIAS CONFIGURATION
A mathematical solution could be obtained simply by substituting into Shockley’s equation as follows:
mathematical approach
The graphical approach

## Slide 17
SELF-BIAS CONFIGURATION
The graphical approach
The second point requires that a level of VGS or ID be chosen and the corresponding level of the other quantity be determined.
The resulting levels of ID and VGS will then define another point on the straight line and permit the drawing of the straight line.
For example, that we choose a level of ID equal to one-half the saturation level.
The straight line is then drawn and the quiescent point obtained at the intersection of the straight-line plot and the device characteristic curve.
The quiescent values of ID and VGS can then be determined and used to find the other quantities of interest

## Slide 18
SELF-BIAS CONFIGURATION
The level of VDS can be determined by applying Kirchhoff’s voltage law to the output
circuit, with the result that

## Slide 19
SELF-BIAS CONFIGURATION

## Slide 20
SELF-BIAS CONFIGURATION
Determine the following for the network

## Slide 21
SELF-BIAS CONFIGURATION
Determine the following for the network

## Slide 22
SELF-BIAS CONFIGURATION
Sketching the device characteristics for the JFET
Determining the Q-point for the network

## Slide 23
SELF-BIAS CONFIGURATION

## Slide 25
VOLTAGE-DIVIDER BIASING
The basic construction is exactly the same as BJT, but the dc analysis of each is quite different. IG = 0 A for FET amplifiers
Since IG = 0 A, Kirchhoff’s current law requires that IR1 = IR2

## Slide 26
VOLTAGE-DIVIDER BIASING

## Slide 27
VOLTAGE-DIVIDER BIASING
Effect of RS on the resulting Q-point.

## Slide 28
ENHANCEMENT-TYPE MOSFETs
Recall that for the n -channel enhancement-type MOSFET, the drain current is zero for levels of gate to- source voltage less than the threshold level VGS(Th), as shown in Figure.
For levels of V GS greater than VGS(Th), the drain current is defined by
Since specification sheets typically provide the threshold voltage and a level of drain current (ID(on)) and its corresponding level of VGS(on),

## Slide 29
Feedback Biasing Arrangement
Since IG = 0 mA, VRG = 0 V and the dc equivalent network
DC equivalent of the network
Determining the Q-point for the network

## Slide 30
Determine IDQ and VDSQ for the enhancement-type MOSFET

## Slide 31
Determine IDQ and VDSQ for the enhancement-type MOSFET
Determining the Q-point for the network

## Slide 32
Voltage-Divider Biasing Arrangement
The fact that IG = 0 mA results in the following equation for V GG as derived from an application of the voltage-divider rule:
Since the characteristics are a plot of ID versus VGS and relates the same two variables, the two curves can be plotted on the same graph and a solution determined at their intersection.
Once IDQ and VGSQ are known, all the remaining quantities of the network such as VDS, VD, and VS can be determined.

## Slide 33
Voltage-Divider Biasing Arrangement
Device

## Slide 34
Voltage-Divider Biasing Arrangement

## Slide 35
Voltage-Divider Biasing Arrangement

## Slide 36
COMMON-GATE CONFIGURATION
The next configuration is one in which the gate terminal is grounded and the input signal typically applied to the source terminal and the output signal obtained at the drain terminal as shown
Two versions of the common-gate configuration.

## Slide 37
COMMON-GATE CONFIGURATION
The next configuration is one in which the gate terminal is grounded and the input signal typically applied to the source terminal and the output signal obtained at the drain terminal as shown
Determining the Q-point for the network

## Slide 38
COMMON-GATE CONFIGURATION
The next configuration is one in which the gate terminal is grounded and the input signal typically applied to the source terminal and the output signal obtained at the drain terminal as shown

## Slide 39
Determine the following for the common-gate configuration
Choosing ID = 6 mA
VGS = -IDRS = -(6 mA)(680 ) = -4.08 V
The device transfer curve is sketched