## Slide 1
Field-Effect Transistors
Become familiar with the construction and operating characteristics of Junction Field Effect (JFET), Metal-Oxide Semiconductor FET (MOSFET),
Be able to sketch the transfer characteristics from the drain characteristics of a JFET, MOSFET,
The BJT transistor is a current-controlled device as depicted in Fig. 6.1a ,
whereas the JFET transistor is a voltage-controlled device as shown in Fig. 6.1b .

## Slide 2
Types of FET’s
JFET – Junction Field Effect Transistor
MOSFET – Metal Oxide Semiconductor Field Effect Transistor
  D-MOSFET - Depletion Mode MOSFET
  E- MOSFET - Enhancement Mode MOSFET

## Slide 3
Construction of the n -channel JFET
There are two types of JFET’s: n-channel and p-channel. The n-channel is more widely used.
There are three terminals: Drain (D) and Source (S) are connected to n-channel Gate (G) is connected to the p-type material

## Slide 4: JFET Operating Characteristics
VGS = 0 V, VDS -Some Positive Value
The instant the voltage VDD (= VDS) is applied, the electrons are drawn to the drain terminal, establishing the conventional current ID with the defined direction of Fig. 6.5 .
The path of charge flow clearly reveals that the drain and source currents are equivalent (ID = IS). Under the condition
In Fig. 6.5 , the flow of charge is relatively uninhibited and is limited solely by the resistance of the n -channel between drain and source.

## Slide 5: JFET Operating Characteristics
VGS = 0 V, VDS -Some Positive Value
It is important to note that the depletion region is wider near the top of both p –type materials.
Assuming a uniform resistance in the n -channel, we can break down the resistance of the channel into the divisions appearing in Fig. 6.6
The result is that the upper region of the p -type material will be reverse-biased by about 1.5 V, with the lower region only reverse-biased by 0.5 V.
Recall from the discussion of the diode operation that the greater the applied reverse bias, the wider is the depletion region
The fact that IG = 0 A is an important characteristic of the JFET.

## Slide 6: JFET Operating Characteristics
VGS = 0 V, VDS Some Positive Value
As the voltage V DS is increased from 0 V to a few volts, the current will increase as determined by Ohm’s law and the plot of I D versus V DS will appear as shown in Fig. 6.7.
The more horizontal the curve, the higher the resistance, suggesting that the resistance is approaching “infinite” ohms in the horizontal region.
If VDS is increased to a level where it appears that the two depletion regions would“touch” as shown in Fig. 6.8 , a condition referred to as pinch-off will result. The level of VDS that establishes this condition is referred to as the pinch-off voltage and is denoted by VP , as shown in Fig. 6.7 .

## Slide 7: JFET Operating Characteristics
VGS = 0 V, VDS Some Positive Value
As VDS is increased beyond VP , the region of close encounter between the two depletion regions increases in length along the channel, but the level of ID remains essentially the same.
In essence, therefore, once VDS > VP the JFET has the characteristics of a current source.
As shown in Fig. 6.9 , the current is fixed at ID = IDSS, but the voltage VDS (for levels > VP ) is determined by the applied load.
The choice of notation IDSS is derived from the fact that it is the drain-to- source current with a short-circuit connection from gate to source.
IDSS is the maximum drain current for a JFET and is defined by the conditions VGS = 0 V and VDS > |VP| .

## Slide 8: JFET Operating Characteristics
V GS < 0 V
The voltage from gate to source, denoted VGS , is the controlling voltage of the JFET.
Just as various curves for IC versus VCE were established for different levels of IB for the BJT transistor, curves of ID versus VDS for various levels of VGS can be developed for the JFET

## Slide 9: JFET Operating Characteristics:
p -Channel Devices
For the p -channel device, the channel will be constricted by increasing positive voltages from gate to source and the double-subscript notation for VDS will result in negative voltages for VDS on the characteristics of Fig. 6.13 , which has an IDSS of 6 mA and a pinch off voltage of VGS = +6 V.
The region to the right of the pinch-off locus of Fig. 6.11 is the region typically employed in linear amplifiers

## Slide 10: JFET – Symbols

## Slide 11: JFET Operating Characteristics
There are three basic operating conditions for a JFET:
JFET’s operate in the depletion mode only
VGS = 0, VDS is a minimum value depending on IDSS and the drain and source resistance
VGS < 0, VDS at some positive value and
Device is operating as a Voltage-Controlled Resistor
For an n channel JFET, VGS may never be positive*
For an p channel JFET, VGS may never be negative*

## Slide 13: N-Channel JFET Operation
The nonconductive depletion region becomes thicker with increased reverse bias.
(Note: The two gate regions of each FET are connected to each other.)

## Slide 14: ID  IDSS
As VGS becomes more negative:
    • the JFET will pinch-off at a lower voltage (Vp).
• ID decreases (ID < IDSS) even though VDS is increased.
• Eventually ID will reach 0A. VGS at this point is called Vp or VGS(off).
• Also note that at high levels of VDS the JFET reaches a breakdown situation. ID will increases uncontrollably if VDS > VDSmax.

## Slide 15
Symbols
VGS = 0 V, ID = IDSS ;
cutoff (ID = 0 A) VGS less than the pinch-off level;
ID is between 0 A and IDSS for VGS 0 V and greater than the pinch-off level.

## Slide 16
TRANSFER CHARACTERISTICS

## Slide 17
TRANSFER CHARACTERISTICS
Applying Shockley’s Equation

## Slide 18
TRANSFER CHARACTERISTICS
It should be obvious from the above that given IDSS and VP (as is normally provided on specification sheets), the level of ID can be found for any level of VGS .
Conversely, by using basic algebra we can obtain [from Eq. (6.3)] an equation for the resulting level of VGS for a given level of ID. The derivation is quite straightforward and results in

## Slide 19
TRANSFER CHARACTERISTICS
Shorthand Method

## Slide 22
IMPORTANT RELATIONSHIPS